The Strak Machine

Reference

Matthias Boese V1.0, 21.09.2020

This reference gives a brief and concise overview of all functions included in the Strak Machine and should therefore be used in addition to the short instruction, which describes the basic operation, installation and use.

1. Parameters of the Strak Machine

The Strak Machine uses a configuration file called "strakdata.txt" in the „ressources“ folder, which contains all necessary configuration data.

The parameters contained there are used to formulate the basic "job" of the Strak Machine (which one is the root airfoil, how many strak airfoils are to be created, which are the relevant Reynolds- numbers), and will be also used to adapt the operation of the Strak Machine to the specific requirements of the user.

The parameters of the Strak Machine can be roughly divided into necessary parameters, which have to be adjusted by the user according to his project, and optional parameters, which can be understood as "expert settings" and are preset with default values.

1.1 Necessary Parameters

The following is a list of the necessary parameters already described in the document "Strak Machine Short instruction".

"xoptfoilTemplate"
The name of the template-file, that will be used in order to generate the input-files for Xoptfoil that are necessary for the airfoil-generation.
The name must be written without the ending „.txt“.
The file can be found in the „ressources“ folder.
The files “iOpt.txt” and “iOpt_HH.txt” will be included in the Strak Machine to use as a reference.
“iOpt.txt” will use “camb-thick-plus” airfoil-shaping functions, “iOpt_HH.txt” will use “Hicks-Henne” airfoil shaping functions.
Using “camb-thick-plus” is faster than using “Hicks-Henne”, but has more limitations concerning the possible solution space and thus in some cases will not accurately achieve the desired target-polars.
The advanced user also can provide his own template file here.

"seedFoilName"
The name of the airfoil-file that will be used as the root-airfoil
The name must be written without the ending „.dat“.
The airfoil-data has to be provided as an ASCII-textfile in selig-format and must be located at the „ressources“ folder.

"optimizeAlphaCl0"
This parameter tells the Strak Machine, whether to carry out an optimization for the zero lift angle (try to keep the same zero lift angle for the airfoil as the root airfoil has).
When the difference in Re between root-airfoil and the following airfoils increases, it may be necessary to switch off this optimization or otherwise the generated airfoil gets too much deformed.

Please Note: This parameter always has to be provided as a list (using [..,..] notation)

"minCLGain"
This trim-value will move the most lower point of the target polar to the left or right (if you look at the „CL over CD“ - graph).

Please Note: This parameter always has to be provided as a list (using [..,..] notation)

"maxSpeedGain"
This trim-value will move the point of lowest drag of the target-polar to the left or right (if you look at the „CL over CD“ – graph).

Please Note: This parameter always has to be provided as a list (using [..,..] notation)

"maxGlideGain"
This trim-value will move the point of best lift/ drag of the target-polar to the left or right (if you look at the „CL over CD“ – graph) or up and down, if you look at the „CL/ CD over CL“-graph.

Please Note: This parameter always has to be provided as a list (using [..,..] notation)

"maxLiftGain"
This trim-value will have an influence on the operating point with the highest lift of the target polar.
The point can be moved to the left or right (if you look at the „CL over CD“ – graph) or up and down, if you look at the „CL/ CD over CL“-graph.

Please Note: This parameter always has to be provided as a list (using [..,..] notation)

"maxGlideShift"
The value of „maxGlideShift“ specifies a CL-difference for shifting the maxGlide-point (change CL of the maxGlide point).

Please Note: This parameter always has to be provided as a list (using [..,..] notation)

„reynolds“
A list of numbers that represent ReSqrt(CL)-values for a type 2 polar calculation, the number of list-elements equals the overall number of airfoils.

The first number belongs to the root-airfoil, the following numbers belong to the following airfoils that shall be created.

Please Note: For a correct function of the Strak Machine the numbers must be sorted in descending order.
This parameter always has to be provided as a list (using [..,..] notation)

"maxReynoldsFactor"
This factor will be used to limit the maximum Reynolds-number that is used for the analysis of the airfoil.

The Strak-machine will always carry out two polar-calculations for each number that is specified in the „reynolds“-list.

1. Type 2-polar-calculation with ReSqrt(CL) = number specified in the „reynolds“-list
2. Type 1-polar-calculation with Re = maxReynoldsFactor * number specified in the „reynolds“-list

1.2 Optional Parameters

Next follows here now a list of optional parameters, which include additional "expert settings".
If necessary, these parameters can be inserted at any position or in any order in the file "strakdata.txt".
If these parameters are not specified by the user in "strakdata.txt", internal default values are used.
The respective default value is therefore specified for each parameter in this description

After starting the Strak Machine in a commandline window you will also see a „Note“-Message displayed for each optional parameter, that has not been mentioned within „stradata.txt“.

The „Note“-Message will also show the default-value.

„bachfileName“
You can specify your own desired name for the batchfile here, that will be used to execute the creation of all strak-airfoils, if you are not satisfied with the default name.

Default-value: „make_strak.bat“

„xoptfoilInputFileName“
The Strak Machine will create an xoptfoil-input-file for each of the strak-airfoils that shall be created, what will be stored in the „build“-folder.
By default, the name of each input file will be „istrak_...k.txt“ where ...k stands for the specified type2 Reynolds-number of the airfoil (e.g. „istrak_220k.txt“)
If you are not satisfied with „istrak“ as a prefix, you can change it here.

Default-value: „istrak.txt“

„operatingMode“
At the moment, it is possible to choose between two different modes for operating the Strak Machine.
The first mode is the "default" mode and is used to create a set of airfoils which is derived from a root airfoil (the „normal“ operation of the Strak Machine).
Everything described so far here and also in the short instruction refers to this default mode.
For development and verification purposes there is another mode, this is the so-called "matchpolarfoils" mode.
Analogous to the "matchfoils" mode in Xoptfoil, this mode is used to convert a given profile into another using the optimizer.
Only in this case not in a direct way directly using the airfol coordinates, but via the detour of the airfoil polars.
This is a very interesting experimental mode.
In this way it can be determined, for example, how exactly the geometric data of an airfoil can be reconstructed from the airfoil polars with the help of the optimizer.
Another, future mode could be that first the root airfoil is created, e.g. based on target values from an Excel spreadsheet, and then the other airfoils are created on this basis.

Default-value: „default“

„xmlFileName“
This parameter is currently of experimental character and serves the purpose of importing a given wing geometry, which is available as an XML file in XFLR5 format, and then automatically deriving the required Reynolds numbers from it.
Currently the XFLR5 file must contain the complete "plane" as data, so that the xml-parser can correctly assign the data to the main wing.

Default-value: None

„numOpPoints“
The polar of the root airfoil is mapped using discrete points, which are distributed as evenly as possible on the polar by a special algorithm.
The number of points used for this can be set with this parameter.
It should be noted that the number of points always includes one point for the definition of the zero lift angle, which is always counted (regardless, if the optimisation for this angle is sitched off, or not).
 However, this point is not displayed in the graphic windows of the Strak Machine.
The number of points has a linear effect on the calculation time xoptfoil needs for the calculation (the more points, the higher the calculation time), but also has an effect on the accuracy with which the polars of the root profile can be mapped (the more points, the more accurate).
A compromise should be sought here between the required calculation time and the desired quality of the result.

Default-value: 16

„CL_min“
This parameter determines the minimum value of CL from which on an analysis of the root airfoil is performed.
This value is also the starting point of all target-polars.
Depending on the requirements of the range of lift which shall be included in the analysis, this parameter can be adjusted.

Default-value: -0.1

„weightingMode“
A „weighting“ must be assigned to each operating point in the xoptfoil-inputfile (for more information please refer to the xoptfoil-reference).
This is done automatically by the Strak Machine.
Since a variable number of operating points is specified with the help of an automatism, it is also necessary to specify the weighting of the operating points automatically.
For this purpose two different algorithms can be selected.
In the mode "sinus" a sinusoidal distribution of the weighting with a maximum in the maxGlide point is given.
Especially when using the profile generation "camb-thick-plus" this weighting mode has proved to be very useful.
If this weighting mode has been selected, the maximum and minimum weighting can also be specified separately (see the following parameters "maxWeight", "minWeight").
Theoretically it also would be possible to do the weighting "inverse" (with a minimum in the point maxGlide)
In the "constant" mode, a constant weighting is specified for all operating points.
The parameters "maxWeight", "minWeight") are irrelevant in this case.

Default-value: „sinus“

„minWeight“
The minimum value used for weighting.
Only relevant if "weightingMode": "sinus" is selected.

Default-value: 0.7

„maxWeight“
The maximum value used for weighting.
Only relevant if "weightingMode": "sinus" is selected.

Default-value: 1.5

„maxLiftDistance“
Im Rahmen der Polaren-Berechnung mittels XFOIL kann es insbesondere im Bereich hoher CL-Werte zu Konvergenz-Problemen kommen. Dies bedeutet die Berechung der Polare in diesem Betriebspunkt konnte nicht erfolgreich durchgeführt werden und die berechneten Werte weisen eine hohe Abweichung / Ungenaugkeit auf und können für eine genaue Analyse des Profils im Prinzip nicht verwendet werden.
Der Parameter „maxLiftDistance“ legt einen Sicherheitsabstand für den Punkt auf der Target-Polaren mit dem höchsten Auftriebsbeiwert vom Punkt der Polaren des Wurzelprofiles, welcher den höchsten Auftriebsbeiwert aufweist.