The Strak Machine

Short Instruction

Matthias Boese 2020

This short instruction will explain some basic functions of the Strak Machine, that are mandatory for using it.

Please take a look at „Strak_Machine_Reference“ for the full reference of functions that are included in the Strak Machine.

1. Main purpose / function of the Strak Machine

For aerodynamic reasons, the wing of an aircraft very often does not have a rectangular-shape with a constant chord-length all along the wingspan.

When the chord-length changes along the wingspan (even at a fixed airspeed), there will be a change in Reynolds-numbers that is proportional to the change in chord-length.

If the same airfoil is used all along a wing with changing chord-length, this will lead to a loss in performance of the wing, as the airfoil will only have the optimum performance at a certain position-range along the wing-span.

The Strak Machine can help to improve the overall wing-performance by creating a set of airfoils, that are optimized according to the different Reynolds-numbers that occur along the wing-span.

The user specifies a set of Reynolds-numbers for the root-airfoil and for the strak-airfoils, that will be passed to the Strak Machine by a parameter-file („strakdata.txt“).

Each specified Reynolds-number (except for the Reynolds-number of the root-airfoil, which is the first), will lead to a new airfoil to be created that is optimized for this Reynolds-number.

In order to get the parameters to control the optimizer (which is Xoptfoil-JX) for creating the new airfoil, the root-airfoil will first be analyzed at the given Reynolds-numbers, using Xfoil to carry out polar-calculations.

The polars of the root-airfoil will be imported by the Strak Machine and a set of proposed target-polars for the new airfoils will be calculated.

The user can apply trim-values to each single target-polar to adapt the shape of the polar to his needs.

The target-polars will be used to generate input-files for Xoptfoil-JX, that will carry out the desired optimizations and will create the new airfoils.

2. Two different Versions: „Strak Machine pure“ / „Strak Machine instant“

As the current implementation of the Strak Machine is based on Python 3.x , usually a Python-Distribution and additional packages have to be installed in order to use it.

Also several paths (e.g. for the python-interpreter) have to be set and in some cases the windows-registry has to be patched, so that the command-line-arguments will be properly passed towards the python-interpreter.

Additional packages, like matplotlib, numpy, a Fortran-namelist-parser etc. have to be installed.

To improve „ease-of-use“ for those users, who do not have much experience with python, there will be a precompiled version of the strak-machine, that will run without having to install python.

This first version is called „Strak Machine instant“.
The Download-size of this version will be larger, as all necessary Python-scripts will be included in the „compiled“ .exe-version.
This version also is portable could even be started from an USB-stick.
But it should be mentioned here, that the starting time of this version is a little bit longer, because the exe-files will be automatically unzipped after starting them.

The second version „Strak Machine pupe“ is for advanced users, who already have a python-installation, know how to install additional packages and so can take advantage of the smaller download size.

Both versions feature the same functions.

3. Getting Started

Before getting started, in case of „Strak Machine pure“ you may have to install Python.
You can follow the steps 3.1.. 3.4 to complete the installation.
In case of „Strak Machine instant“ you can directly jump to step 3.5.

3.1 Strak-Machine pure: installing a Python-Distribution
Strak machine pure requires a Python 3.x-Installation.

The installation can either be downloaded from https://www.python.org/downloads/
or you can use „Python-Anaconda“, which is a bigger distribution that already includes the package „matplotlib“.

3.2 Strak-Machine pure: Installing additional packages

After you have installed Python 3.x, you have to install the following additional packages using the „pip install“ command in the windows commandline:

pip install f90nml
pip install colorama
pip install termcolor

If you did not choose Anaconda, but a smaller Python-Distribution, you will also have to execute:
pip install matplotlib

Note: In some python-versions a specific version of matplotlib is required, as there are dpendencies between the packages.

There is a specific pip-command to install a certain version of a package (hint: type „pip –help“ to get all features of pip).

3.3 Strak-Machine pure: patching the windows registry

You may have to patch the windows registry in order to get the commandline-arguments correctly passed to the python-interpreter.

To do this, open „RegEdit“ and navigate to HKEY_CLASSES_ROOT\Applications\python.exe\shell\open\command.
Right click on name (Default) and Modify. Enter (for Example):
"C:\ProgramData\Anaconda3\python.exe" "%1" %*

3.4 Strak-Machine pure: setting the path environment-variable

The path to the Python-Interpreter that you have installed has to be included in the „path“-environment-variable.

3.5 Both versions of Strak Machine: unzip the archive

Unzip the zip-archive „strakmachine_instant.zip“ or strakmachine_pure.zip“ to your desired location.

Inside the unzipped folder you will find a complete runnable version that is setup with an example „SD-strak“.

3.6 Starting the Strak Machine

Now you are ready to take a first look.

Start the batchfile „start_strakmachine.bat“

If every previous step was carried out correctly, the next thing you should see is a window showing the analysis of the „SD-airfoil“:

The main-window will be divided into four sub-windows.
You should see the strak-machine-logo in the upper left sub-window and three polar-graphs in the other sub-windows.

The contents of the polar-graph-windows will be explained later.

You will also find a small toolbar that allows navigation like „zooming“ and „scrolling“ in each of the sub-windows and you also can save an image of the main window to disk.

Feel free to try out.

4. The configuration-file „strakdata.txt“

When started, the Strak Machine will first automatically read the file „strakdata.txt“ from the „ressources“-folder.

This is an ASCII-textfile in so called „json“-format, that contains a configuration for the Strak Machine, telling it for example which airfoil to take as a root-airfoil and which polar-calculations to carry out.

This file has to be adapted by the user for his own project.

When you open the file in a text-editor, you should now see the following (without the red additions of course, which have only been added for explanation purposes):

This example file of „strakdata.txt“ does not contain the complete set of parameters of the Strak Machine, but only mandatory parameters that must be set by the user.

Further parameters can be added by on demand.

Other optional parameters, that are not shown here, will be used with internal default values, they will be described in the „Strak_Machine_Reference“.

The order of the parameters / sorting of the lines can be changed without having an effect on the function of the Strak Machine (if you would like to have a different sorting, you can do that).

Now a short explanation of the mandatory parameters:

„xoptfoilTemplate“
The name of the template-file, that will be used when generating the input-file for xoptfoil.
The file can be found in the „ressources“ folder.
In this case, a template file will be used to carry out the airfoil-optimization using „Hicks-Henne“ functions.
The advanced user also can provide his own template file here.

„seedFoilName“
The name of the airfoil-file that will be used as the root-airfoil (the name must be written here without the ending „.dat“).
The airfoil-data has to be provided as an ASCII-textfile in selig-format and must be located at the „ressources“ folder.

„reynolds“
A list of numbers that represent ReSqrt(CL)-values for a type 2 polar calculation, the number of list-elements equals the overall number of airfoils.

The first number belongs to the root-airfoil, the following numbers belong to the follow-up airfoils.

For a correct function of the strak Machine the numbers must be sorted from large to small (that may be improved in upcoming versions but is a restriction today).

The Strak Machine mainly works with type 2 (fixed lift) polars.
This means, that the number that is entered here, will be represent Re@CL = 1.0 and will be implicitly changed when CL changes.

The function Re(CL) is hyperbolic, that means when CL gets smaller, Re will get infinite, the graph
shows an example:

T

To keep Re limited to values that will probably occur during flight, the Strak Machine will set a limit, that will be determined from „reynolds“ and „maxReynoldsFactor“.

„maxReynoldsFactor“
This factor will be used to limit the maximum Reynolds-number that is used for analysing the airfoil.

The Strak-machine will always carry out two polar-calculations for each number that is specified in the „reynolds“-list.

1. Type 2-polar with ReSqrt(CL) = number specified in the „reynolds“-list
2. Type 1-polar with Re = maxReynoldsFactor * number specified in the „reynolds“-list

In the example-file, maxReynoldsFactor is set to 2.0, and ReSqrt(CL) for the root-airfoil is set to 220000.

So the Strak Machine will perform a Type 2 polar calculation with ReSqrt(CL) = 220000 and a Type 1 polar calculation with Re = 440000.

For the airfoil-analysis, these two polars will be merged automatically by the Strak Machine to a mixed Type 1 / Type 2 polar that will be displayed in the three graphs.

You can see in the change of the colour, where the polar changes from Type 1 to Type 2.

The switching between the two polar-types will occur at a certain CL, ,that will be automatically calculated from „maxReynoldsFactor“ (merging-point).

„optimizeAlphaCL0“
This parameter tells the Strak Machine, whether to carry out an optimization for the zero lift angle (try to keep the same zero lift angle for the airfoil as the root airfoil has).

The zero lift angle is the angle of attack of a wing profile against the airflow, where neither lift nor downforce is generated.

The zero lift angle also strongly determines the maximum lift.

When the difference in Re between root-airfoil and the following airfoils increases, it may be necessary to switch off this optimization or otherwise the generated airfoil gets to much deformed.

It is recommended to keep this optimization activated along the wing as long as possible.

The „trimming“ parameters ...Gain and ...Shift

The next five parameters are used for trimming the „target- polars“, that are calculated by the Strak Machine.

The concept of the Strak Machine is to setup a target-polar for each of the following-airfoils that shall be created.

The target-polar-information will be passed to Xoptfoil-JX by a parameter-file for each airfoil and the airfoil will be optimized to match the target-polar information.
The target-polar mainly consists of discrete Lift/Drag-operating points at a certain Reynolds-number.

When you look in the main-window of the Strak Machine, you will find the target“-polars as yellow-dotted lines inside of the two lower graphs (the discrete points being connected by straight lines).

You should also find this in the legend.