 Xfoil_worker v1.52.0
## Reference

Jochen Guenzel 2020
Xfoil_worker is a small command line tool to do various tasks around airfoil optimization. It is especially useful for automization of the optimization process.

Usage:
Xfoil_worker -w worker_action [Options]
Folllowing actions are supported
-w polars Generate polars for an airfoil
-w norm Repanel and normalize an airfoil
-w smooth Repanel, normalize and smooth an airfoil
The options for the various actions are described in the following sections.

###### Generating polars ( -w polars)

A defined polar for an airfoil will be generated in Xfoils polar format. The polar file is ready to be imported into xflr5 or flow5 via the menu function “Polars / Import Xfoil Polar(s). The definition for the polar and Xfoils initial parameters are defined in an Xoptfoil input file. Please find the description of the parameters in the Xoptfoil(-JX) documentation.
Command line options used for polar generation:
-i input_file	Name of an Xoptfoil input file to read the settings for the polar generation. Only the following namelists are needed for polar generation: / &polar_generation / Settings for polar: polar type, based on cl oder alpha, value range / &xfoil_run_options - optional / Options for Xfoils aerodynamic calculations. Normally the default values are fine, so this namelist is optional / &xfoil_paneling_options - optional / Options for Xfoils repaneling which is done prior to the polar generation. Normally the default values are fine, so this namelist is optional
[-r xxxxxx]	The desired Reynolds number of the polar. If the Reynolds number is not defined in the input file, the value is taken from this command line option. This is useful to have a single input file for different Reynolds numbers
-a airfoil_file	The name of the airfoil file
-o output_prefix	The generated polar will be written to the subdirectory / .\output_prefix_polars

Example:
Xfoil_worker -i iPolars.txt -r 600000 -a RG15.dat -o RG15
###### Repanel and normalize an airfoil ( -w norm)

An airfoil will be repaneled by Xfoils PANGEN routine and normalized to have the leading edge at 0,0 and the trailing edge at 1,0. The new airfoil will have 7 decimals in the .dat file.
In addition to the new airfoil .dat file, a file output_prefix_design_coordinates.dat will be generated which allows to inspect the result of repanel and normalize with Xoptfoil_visualizer-JX.
Command line options used for polar generation:
[-i input_file]	- optional - Name of a Xoptfoil input file to read the settings for repaneling. Only the following namelists are used for repaneling: / &xfoil_paneling_options - optional - / Options for Xfoils repaneling. Normally the default values are fine. / If the input file or a namelist is missing default values will be taken.
-a airfoil_file	The name of the airfoil file
-o output_prefix	Name of the smoothed airfoil. Following files will be generated / output_prefix.dat / output_prefix_design_coordinates.dat

Example:
Xfoil_worker -w norm -a RG15.dat -o RG15_smoothed
###### Smooth an airfoil ( -w smooth)

An airfoil will be repaneled by Xfoils PANGEN routine, normalized and smoothed by Xoptfoil-JX smoothing algorithm (‘Chaikin Corner Cut’). This action is useful either in preparing an airfoil for optimization or to improve the geometric quality of your airfoil collection.
In addition to the new airfoil .dat file, a file output_prefix_design_coordinates.dat will be generated which allows to inspect the result of repaneling, normalizing and smoothing with Xoptfoil_visualizer-JX.
Command line options used for polar generation:
[-i input_file]	- optional - Name of an Xoptfoil input file to read the settings for repaneling and smoothing. Only the following namelists are used for smoothingn: / &smoothing_options - optional / Define spike_threshold. / &constraints - optional / Define curv_threshold and highlow_threshold / &xfoil_paneling_options - optional / Options for Xfoils repaneling which is done prior to tsmoothing. Normally the default values are fine, so this namelist is optional
-a airfoil_file	The name of the airfoil file
-o output_prefix	Name of the smoothed airfoil. Following files will be generated / output_prefix.dat / output_prefix_design_coordinates.dat

Example:
Xfoil_worker -w smooth -i iSmooth.txt -a RG15.dat -o RG15_smoothed